Nixi Tube Clock
# Arduino Code Documentation
Release tbd

This document contains detailed Arduino code documentation for the MGRA & AFCH Nixi Tube clock, model Arduino Shield Nixie IN-14 Musescore plugin. Within the code are reference numbers in the form of CD-##. Those are pointers to the matching reference ID number within this document.
## Outstanding TO-DOs
Ref#	TO-DO Description
	LED Tuning. Adjust backlight NeoPixle LEDs for desired color and intensity. Esp the LED under the blinking dots tower.
	EU/US Date Flip. The thing where the euro date format shows first for a flash, then it flips to the US date format.
	Create Night Sleep Timer: Create code to put the display tubes to sleep at night, and auto-wake up in the morning.

## Code Documentation
Ref#	Documentation
CD-01	Turn Off Arduino Internal Green LED & Remove IR Remote Feature. This is harder than it looks. Turns out that the Arduino SPI SCK and MOSI signals at pins D51 & D52 have been tied to pins D11 and D13. You can see this is the schmatic. So if you mess with pin-13, which is the hard-coded pin that the Arduino internal LED is connected to, you interfere with the clock signal for the IC which drives the nixi tube display segments (the HV57708 chip). I asked GRA/AFCH about this: / “We do not use pin 13 in our Clocks in our current configuration. And the connection is made for compatibility reasons between the UNO and MEGA, including the older versions.” / So based on this I bent over the header pin that connects into the Arduio at pin-13, such that it no longer connects into the Arduino, so that I could control PIN-13 from the Arduino code and turn that LED off in the setup code. / BUT – it also turns out that deep in the code for the infrared remote control feature is a function that blinks the internal LED on pin-13. This is inside Irremote.h. Line 81 is: # define BLINKLED 13. / Since I will never use an IR remote with this clock I have removed all the code associated with the IR remote control. / KEY LEARNING-A: / Last Update: 2023-02-12
CD-02
CD-03
CD-04
CD-05
CD-06