Nixi Tube Clock
# Arduino Code Documentation
Release tbd

This document contains detailed Arduino code documentation for the MGRA & AFCH Nixi Tube clock, model Arduino Shield Nixie IN-14 Musescore plugin. Within the code are reference numbers in the form of CD-##. Those are pointers to the matching reference ID number within this document.
## Outstanding TO-DOs
Ref#	TO-DO Description
	EU/US Date Flip. The thing where the euro date format shows first for a flash, then it flips to the US date format.
	Create Night Sleep Timer: Create code to put the display tubes to sleep at night, and auto-wake up in the morning.

## Code Documentation
Ref#	Documentation
CD-01	Turn Off Arduino Internal Green LED & Remove IR Remote Feature. This is harder than it looks. Turns out that the Arduino SPI SCK and MOSI signals at pins D51 & D52 have been tied to pins D11 and D13. You can see this is the schmatic. So if you mess with pin-13, which is the hard-coded pin that the Arduino internal LED is connected to, you interfere with the clock signal for the IC which drives the nixi tube display segments (the HV57708 chip). I asked GRA/AFCH about this: / “We do not use pin 13 in our Clocks in our current configuration. And the connection is made for compatibility reasons between the UNO and MEGA, including the older versions.” / So based on this I bent over the header pin that connects into the Arduio at pin-13, such that it no longer connects into the Arduino, so that I could control PIN-13 from the Arduino code and turn that LED off in the setup code. / BUT – it also turns out that deep in the code for the infrared remote control feature is a function that blinks the internal LED on pin-13. This is inside Irremote.h. Line 81 is: # define BLINKLED 13. / Since I will never use an IR remote with this clock I have removed all the code associated with the IR remote control. / Last Update: 2023-02-12
CD-02	RGB LEDs on One Fixed Color. This is a user-configurable feature through the mode setting functions. In the code the variable “LEDsLock” holds this setting. If LEDsLock is TRUE then the backlight LEDs are fixed on one color. The setting of LEDsLock is persistently stored in the EEPROM. If LEDsLock is TRUE, then the RDG LED colors are set from the R, G, B values that are stored in EEPROM. So you’ll see, for example: if (LEDsLock == 1) setLEDsFromEEPROM(); And void setLEDsFromEEPROM() is defined in the module rotateFireWorks_SK.ino.
CD-03	Intensity of RGB LED Under the Blinking Dots Column. Because, for me, the LED that is under the blinking dots column shines too bright, and interferes with the appearence of the blinking dots I created ability to lower the intensity of the RGB-LED under the dots column. / NOTE-1: Since I have the 4-digit clock (HH:MM) I did not attempt to make the code work for clocks with two dot columns. / NOTE-2: I hard-coded an intensity adjustment into my patch. There is no provision for a user-configurable setting via the back panel controls. To adjust the intensity you have to change the code in the the rotateFireWorks_SK.ino module. / Note-3: As I find the rotating color changes of the LEDs default behavior to be too distracting, I have set my clock to display only a single LED backlight color. Thus I have attempted to add this change to the color rotation code. However, doing so is probably just a matter of copying the code change I made in setLEDsFromEEPROM() over to the rotateFireWorks() function. / Taking note of CD-02 above, this change is implemented via updates to code that is in the rotateFireWorks_SK.ino file. / Approach: In the loop where the LED colors are set and displayed, inside of setLEDsFromEEPROM(), I reduce each R,G,B color value for the column’s pixel by the #define COLdim statement at the top of the rotateFireWorks_SK.ino file. Reducing the value of each color has the effect of retaining the set color, but dimming the brightness. / Last Update: 2023-03-02
CD-04
CD-05
CD-06